## Slide 1: JNCIS-ENT
Intermediate System to Intermediate System (IS-IS)

## Slide 2: Monitoring IS-IS
Operating and Troubleshooting IS-IS
5

## Slide 3: Interface Status
ben@R1> show isis interface detail
IS-IS interface database:
ge-0/0/0.0
Index: 69, State: 0x6, Circuit id: 0x2, Circuit type: 1
LSP interval: 100 ms, CSNP interval: 10 s
Adjacency advertisement: Advertise
Level Adjacencies Priority Metric Hello (s) Hold (s) Designated Router
1 1 64 10 3.000 9 R1.02 (us)
lo0.0
Index: 72, State: 0x6, Circuit id: 0x1, Circuit type: 0
LSP interval: 100 ms, CSNP interval: disabled
Adjacency advertisement: Advertise
Level Adjacencies Priority Metric Hello (s) Hold (s) Designated Router
1 0 64 0 Passive
2 0 64 0 Passive
ben@R1> show isis interface
IS-IS interface database:
Interface L CirID Level 1 DR Level 2 DR L1/L2 Metric
ge-0/0/0.0 1 0x2 R1.02 Disabled 10/10
lo0.0 0 0x1 Passive Passive 0/0

## Slide 4: Adjacency Status
ben@R1> show isis adjacency
Interface System L State Hold (secs) SNPA
ge-0/0/0.0 R2 1 Up 25 50:0:0:1:0:0
ben@R1> show isis adjacency detail
R2
Interface: ge-0/0/0.0, Level: 1, State: Up, Expires in 23 secs
Priority: 64, Up/Down transitions: 3, Last transition: 00:00:26 ago
Circuit type: 1, Speaks: IP, IPv6, MAC address: 50:0:0:1:0:0
Topologies: Unicast
Restart capable: Yes, Adjacency advertisement: Advertise
LAN id: R1.02, IP addresses: 192.168.1.2

## Slide 5: Viewing LSP Database
ben@R1> show isis database brief
IS-IS level 1 link-state database:
LSP ID Sequence Checksum Lifetime Attributes
R1.00-00 0x8 0xb2b0 1058 L1
R1.02-00 0x6 0x9990 1058 L1
R2.00-00 0x7 0x2c33 1056 L1
3 LSPs
IS-IS level 2 link-state database:
0 LSPs

## Slide 6: Viewing LSP Detailed Database
ben@R1> show isis database detail
IS-IS level 1 link-state database:
R1.00-00 Sequence: 0x8, Checksum: 0xb2b0, Lifetime: 865 secs
IS neighbor: R1.02 Metric: 10
IP prefix: 192.168.1.0/24 Metric: 10 Internal Up
R1.02-00 Sequence: 0x6, Checksum: 0x9990, Lifetime: 865 secs
IS neighbor: R1.00 Metric: 0
IS neighbor: R2.00 Metric: 0
R2.00-00 Sequence: 0x7, Checksum: 0x2c33, Lifetime: 863 secs
IS neighbor: R1.02 Metric: 10
IP prefix: 192.168.1.0/24 Metric: 10 Internal Up
IS-IS level 2 link-state database:

## Slide 7: IS-IS Statistics
ben@R2> show isis statistics
IS-IS statistics for R2:
PDU type Received Processed Drops Sent Rexmit
LSP 164 164 0 326 0
IIH 16239 8 0 48753 0
CSNP 0 0 0 14600 0
PSNP 0 0 0 0 0
Unknown 0 0 0 0 0
Totals 16403 172 0 63679 0
Total packets received: 16403 Sent: 63679
SNP queue length: 0 Drops: 0
LSP queue length: 0 Drops: 0
SPF runs: 166
Flex Algo Full SPF runs: 0
Flex Algo Partial SPF runs: 0
Fragments rebuilt: 328
LSP regenerations: 322
Purges initiated: 0