## Slide 1: JNCIS-ENT
Layer 2 switching and VLANs

## Slide 2: Frame Processing
Switched frame and packet processing
6

## Slide 3: Control and Forwarding Planes
Like other Junos devices, the EX-series switches feature a distinct control plane (RE) and forwarding plane (PFE).
/ BT

## Slide 4: Control and Forwarding Planes
Internal link between RE and PFE is rate limited, it is hard-coded and not able to be modified. PFE updates are a high priority in the kernel and are done incrementally.
/ BT

## Slide 5: Frame Processing – Unknown Source
1
Frame enters ingress port
2
Ingress PFE performs MAC lookup, determined source is unknown.
3
Ingress PFE sends header information to RE where MAC is added or discarded
4
If new MAC added to bridge table, new entry is sent to all PFEs
Notes: MAC may be discarded if port-security / mac limiting is enabled.

## Slide 6: Frame Processing – Known Destination
1
Frame enters ingress port
2
Ingress PFE performs MAC lookup, determines egress PFE and port
3
Ingress PFE forwards frame to egress PFE
4
Egress PFE forwards frame out egress port.
Notes: No additional lookup is done by PFE n.

## Slide 7: Frame Processing – Unk. Destination
1
Frame enters ingress port
2
Ingress PFE performs MAC lookup, determines unknown destination and must flood frame
Ingress PFE and all remote PFEs flood frame out all ports in broadcast domain
3
Notes: No additional lookup is done by PFE n.