## Slide 1: JNCIS-ENT
Layer 2 switching and VLANs

## Slide 2: L2 Switching Lab
Monitoring Layer 2 Switching Operations
9

## Slide 3: Diagram

## Slide 4: Configuring Ethernet Switching
Review the starting configuration on SW1 and SW2
Configure ge-0/0/2 unit 1 on SW2 for ethernet switching
Correct ge-0/0/2 configuration by renaming unit 1 to unit 0
Configure ge-0/0/2 on SW2 as an access port on the default VLAN
Copy the ge-0/0/2 configuration to ge-0/0/1 and ge-0/0/3 on SW2
Commit the configuration and validate
Configure ge-0/0/1-ge-0/0/3 as an interface range as access ports on the default VLAN
Commit configuration and Validate configuration is functional based on designed topology from diagram
  Ping interfaces from SW1 in each routing-instance from the default instance to confirm packets are being switched appropriately on SW2

## Slide 5: Configuring Static MAC Addresses
Review the ethernet-switching table
Clear the table and validate it is cleared
Configure a static MAC table entry on ge-0/0/1-ge-0/0/3 on SW2
  ge-0/0/1 MAC = 00:26:88:11:11:11
  ge-0/0/2 MAC = 00:26:88:22:22:22
  ge-0/0/3 MAC = 00:26:88:33:33:33
Commit and validate changes took effect