## Slide 1: JNCIS-ENT
Layer 2 switching and VLANs

## Slide 2: VLANs
Virtual Local Area Networks
9

## Slide 3: What is a VLAN?
VLANs allow for the segregation of individual ports on a single physical switch into separate broadcast domains
Switch
Broadcast frame
VLAN 10
VLAN 10
VLAN 20
X

## Slide 4: Switchport Designations
Switchports can be configured in either access or trunk mode
  Default configuration sets all ports in access mode in the default VLAN.
VLAN 10
VLAN 10
VLAN 20
VLAN 10
Access Ports
Trunk Port

## Slide 5: Access Ports
Access ports carry untagged traffic for a single broadcast domain
  Typically access ports are ones connecting to end-user devices such as workstations and printers
VLAN 10
VLAN 10
VLAN 20
VLAN 10
Access Ports

## Slide 6: Trunk Ports
Trunk ports carry tagged traffic and can belong to multiple broadcast domains
  Trunk ports are typically ports connecting to other switches or devices which must communicate over multiple VLANs, such as Wireless Access Points and Hypervisors
VLAN 10
VLAN 10
VLAN 20
VLAN 10
Trunk Port

## Slide 7: VLAN Tagging
When traffic is sent over a trunk port, a tag is inserted into the frame header to differentiate which VLAN traffic is being transmitted on
  The receiving switch inspects the tag and processes the incoming frame in the context of the target VLAN
Preamble
Destination Address
Source Address
Type
Data
FCS
Tag
VLAN 10
VLAN 20
VLAN 10