## Slide 1: JNCIS-ENT
Layer 2 switching and VLANs

## Slide 2: Trunking and Voice VLANs
Tagging to differentiate traffic
11

## Slide 3: VLAN Tagging
When traffic is sent over a trunk port, a tag is inserted into the frame header to differentiate which VLAN traffic is being transmitted on
  The receiving switch inspects the tag and processes the incoming frame in the context of the target VLAN
  802.1Q protocol is used to format the tag header field
Preamble
Destination Address
Source Address
Type
Data
FCS
Tag
VLAN 10
VLAN 20
VLAN 10

## Slide 4: Switchport Designations
Switchports can be configured in either access or trunk mode
  Default configuration sets all ports in access mode in the default VLAN.
VLAN 10
VLAN 10
VLAN 20
VLAN 10
Access Ports
Trunk Port

## Slide 5: Configuring Trunk Ports
Trunk ports are configured by setting the interface-mode trunk command at the edit interfaces <intf> unit 0 family ethernet-switching hierarchy
{master:0} [edit]
user@switch# show interfaces ge-0/0/0
description USER;
unit 0 {
family ethernet-switching {
interface-mode trunk;
vlan {
members [default v950];
}
}
}
{master:0} [edit]
user@switch# show interfaces ge-0/0/1
description MGMT;
unit 0 {
family ethernet-switching {
interface-mode trunk;
vlan {
members all;
}
}
}

## Slide 6: VoIP Phone Connectivity
Often end user workstations will connect through desktop VoIP phones for LAN connectivity
  Desktop VoIP phones often have 2 RJ45 ports. 1 for a connection to the LAN switch, another for a connection to a workstation or other end user device.
  Typically, phones reside in a different broadcast domain than workstations, and therefore reside in a different VLAN
VLAN 20
VLAN 10
Preamble
Destination Address
Source Address
Type
Data
FCS
Tag
Tagged
Untagged

## Slide 7: Voice VLANs
VoIP phones can use LLDP-MED (Link Layer Discovery Protocol-Media Endpoint Discovery) TLVs to dynamically learn what VLAN to tag voice and data traffic with.
Voice VLAN is configured in the edit switch-options voip configuration hierarchy
{master:0} [edit switch-options]
user@switch# show
voip {
interface (access-ports | interface-name) {
vlan (vlan-name | vid);
}
}
Configured Voice VLAN for all access ports
or only specific interfaces or interface ranges
Specify the VLAN name or VLAN ID number

## Slide 8: Monitoring Voice VLAN
Although the interface is an Access Port, it will be a member of multiple VLANs if configured with Voice VLAN
{master:0} [edit]
user@switch# show interfaces ge-0/0/0
description USER;
unit 0 {
family ethernet-switching {
interface-mode access;
vlan {
members default;
}
}
}
{master:0} [edit switch-options]
user@switch# show
voip {
interface ge-0/0/0.0{
vlan voice;
}
}
{master:0}
user@switch> show vlans
Routing instance VLAN name Tag Interfaces
default-switch default 10
ge-0/0/0.0*
default-switch voice 20
ge-0/0/0.0*