## Slide 1: JNCIS-ENT
Layer 2 switching and VLANs

## Slide 2: VLAN Lab
Configuring and monitoring VLANs and VLAN trunking
14

## Slide 3: Diagram

## Slide 4: Configuring VLANs on SW2
Review the starting configuration on SW1 and SW2
Perform the following steps on SW2:
Configure the VLAN named v11 with a vlan-id of 11
Configure the VLAN named v12 with a vlan-id of 12
Configure fe-0/0/2 as an access port for v11 VLAN
Configure fe-0/0/3 as an access port for v12 VLAN and commit
Correct fe-0/0/2 and fe-0/0/3 interface configuration referencing commit error
Configure ge-0/0/1 as a trunk port for VLANs v11 and v12
Commit configuration and validate using show vlans

## Slide 5: Configuring VLANs on SW1
Perform the following configuration steps on SW1
Configure ge-0/0/1 as a trunk port for all VLANs
Activate VLAN interface configurations for v11 and v12
Commit the configuration and validate
Activate VLAN configuration for v11 and v12
Commit the configuration
Ping from the default routing instance to VR11 and VR12 to validate trunking and switching is functioning correctly.
Review the effects on the ethernet-switching table on SW2