## Slide 1: JNCIS-ENT
Layer 2 security and loop prevention

## Slide 2: BPDU, Loop and Root Protection
Protecting a layer 2 topology
5

## Slide 3: What If?
A rogue switch on the network is at best an accident which can create costly downtime and be difficult to investigate
  At worst, a malicious actor can use a rogue switch to intentionally create downtime or gain access to unauthorized information
A misconfigured production switch can cause many issues such as slowness or even a loop or outage
  Perhaps you accidentally forget to configure the bridge priority or connect the switch to a mislabeled patch panel port
  Undesired topology changes can be difficult to determine

## Slide 4: BPDU Protection
BPDU Protection is configured on ports which are expected to never connect to another switch
  These would typically be edge ports in RSTP. However, if an edge port receives a BPDU, it will simply start participating in RSTP, unless BPDU Protection is configured
Places a port into a blocking state if a BPDU is received
Akin to Cisco’s BPDU Guard
  Both features essentially function in the same manner
SW2
SW1 Root Bridge
SW3
D
D
R
R
A
D
Rogue Switch
X
BPDU

## Slide 5: Configuring BPDU Protection
BPDU protection can be configured whether (R)STP is enabled or not
SW2
SW1 Root Bridge
SW3
D
D
R
R
A
D
Rogue Switch
X
BPDU
{master:0} [edit protocols rstp]
user@switch2# show
interface ge-0/0/1;
interface ge-0/0/2;
interface ge-0/0/3 {
edge;
}
bpdu-block-on-edge;
{master:0} [edit protocols layer2-control]
user@switch2# show
bpdu-block {
interface ge-0/0/3;
}

## Slide 6: Root Protection
Root Protection is configured on ports which are expected to never be root ports
  These would typically be downstream ports on the aggregation switches.
Places a port into a blocking state if a superior BPDU is received
  This blocking prevents the switch that should not be a root bridge from being elected as the root.
Once superior BPDUs are no longer received, the port will automatically revert to the forwarding state.
SW2
SW1 Root Bridge
SW3
D
D
R
R
A
D

## Slide 7: Configuring Root Protection
An interface can be configured for Root Protection or Loop Protection, but not both.
  Attempting to do so will result in a commit check-out failure
SW2
SW1 Root Bridge
SW3
D
D
R
R
A
D
{master:0} [edit protocols rstp]
user@SW1# show
interface ge-0/0/1.0 {
no-root-port;
}
interface ge-0/0/2.0 {
no-root-port;
}
ge-0/0/1
ge-0/0/2

## Slide 8: What If?
Hardware or software problems on a switch can cause a blocked port to erroneously transition to a designated port
  This can occur due to software problems or hardware problems. If a fiber link becomes unidirectional and continues to transmit, this situation could also occur.
SW2
SW1 Root Bridge
SW3
D
D
R
R
A
D
X
BPDU
SW3 fails to receive BPDUs due to hardware or software failure
SW2
SW1 Root Bridge
SW3
D
D
R
R
D
X
D
Loop

## Slide 9: Loop Protection
Loop protection prevents a blocked/discarding port from transitioning to a forwarding state if BPDUs cease to be received
  Ports which cease to receive BPDUs are transitioned to the ‘loop inconsistent’ role and maintain a blocking/discarding state.
Loop protection should be enabled on all non-designated ports
SW2
SW1 Root Bridge
SW3
D
D
R
R
A
D
X
BPDU
Loop Protection

## Slide 10: Configuring Loop Protection
The alarm function creates a log entry but will not transition port to discarding or blocking state
{master:0} [edit protocols rstp]
user@SW3# show
interface ge-0/0/1 {
bpdu-timeout-action {
alarm;
}
}
interface ge-0/0/2 {
bpdu-timeout-action {
block;
}
}
SW2
SW1 Root Bridge
SW3
D
D
R
R
A
D
X
BPDU
Loop Protection

## Slide 11: Monitoring Loop Protection
user@SW3> show spanning-tree interface
Spanning tree interface parameters for instance 0
Interface Port ID Designated Designated Port State Role
port ID bridge ID Cost
ge-0/0/1 128:2 128:2 32768.4c9614710b50 20000 FWD ROOT
ge-0/0/2 128:3 128:3 32768.4c9614710b51 20000 BLK DIS (Loop-Prev)
user@SW3> show log messages | match “loop”
Dec 11 09:46:51 switch l1cpd[1192]: Loop_Protect: Port ge-0/0/2.0: Received information expired on Loop Protect enabled port