## Slide 1: JNCIS-ENT
Layer 2 security and loop prevention

## Slide 2: Ethernet Ring Protection Switching
ERPS overview and configuration
7

## Slide 3: What is ERPS?
Designed to provide reliable, fast loop-free protection to an Ethernet network in a ring topology
  Sub-50 millisecond convergence time targeted
Defined/Proposed in ITU-T G.8032
Switch2
Switch3
Switch1 RPL Owner
Switch4

## Slide 4: ERPS Overview
Because of the ring topology, if a single link is blocked then the topology becomes loop-free
  This blocked link is the Ring Protection Link (RPL)
  The node which controls the RPL is the RPL owner
In a failure scenario, the RPL owner unblocks the RPL to restore continuity
  Once the failure is repaired, the RPL owner is responsible for re-blocking the RPL
Non-RPL owner nodes also participate in R-APS messages
  Ring Automatic Protection Switching messages are used to signal a state change in the ring
Switch2
Switch3
Switch1 RPL Owner
Switch4
X

## Slide 5: APS Frame Fields
Request / state
  Sent by any node on ring. 0000 indicates no failure, 1011 indicates a failure
Reserved 1
  Always 0000. Reserved for future use
RPL Blocked
  Only signaled by RPL owner. 1 = RPL blocked , 0 = RPL unblocked
Do not flush
  1 indicates nodes should not flush their MAC tables. 0 indicates to flush MAC tables
Status Reserved
  Reserved for future use. Always 000000
Node ID
  MAC address of the sending node
Reserved 2
  Reserved for future use. Always all zeros
Notes: increasing topology changes indicates a loop or flapping link

## Slide 6: ERPS Normal Operation
RPL owner sends R-APS message every 5 seconds by default out all interfaces
  RPL Blocked is set to 1 (RPL blocked)
  Request/State set to 0000 (no failure)
  Do not flush set to 0 (flush)
Ring nodes flush MAC tables once when receiving first R-APS message
  Nodes do not continue to flush on each message. Only the first message.
Switch2
Switch3
Switch1 RPL Owner
Switch4
X
R-APS
R-APS

## Slide 7: ERPS Failure Condition
Nodes detecting a failure send R-APS messages throughout the ring
  Request/State set to 1011 (signal fail detected)
  Do not flush set to 0 (flush)
  Nodes detecting signal fail continue to send R-APS messages every 5 seconds until fixed
RPL owner unblocks RPL when R-APS signaling failure is received
  RPL owner ceases sending R-APS messages until failure condition clears
Ring nodes are in ‘Protection’ state
Switch2
Switch3
Switch1 RPL Owner
Switch4
X
R-APS
R-APS
Link failure
RPL unblocked

## Slide 8: ERPS Restoration
Nodes which detected failure send R-APS message indicating fail cleared
  Request/State set to 0000 (no request)
  Do not flush set to 1 (do not flush)
  Wait to Restore (WTR) timer proceeds
  Nodes that detected failure continue to block links facing the failure
Nodes that detected failure continue to send R-APS messages until a R-APS message is received from the RPL owner
  RPL owner will send a R-APS message once WTR timer completes
  RPL owner will block RPL once WTR timer complete
Once R-APS message received from RPL owner, other links unblocked
  R-APS messages cease from the nodes that detected failure
Switch2
Switch3
Switch1 RPL Owner
Switch4
X
R-APS
R-APS

## Slide 9: Config – RPL Owner
user@switch1> show configuration protocols
protection-group {
ethernet-ring cl-ring-01 {
ring-protection-link-owner;
east-interface {
control-channel {
ge-0/0/0;
}
ring-protection-link-end;
}
west-interface {
control-channel {
ge-0/0/1;
}
}
control-vlan rpsControl;
data-channel {
vlan [2 134];
}
}
}
Switch2
Switch3
Switch1 RPL Owner
Switch4
X
R-APS
R-APS
ge-0/0/1
ge-0/0/0
{master:0} [edit]
user@switch1# show interfaces ge-0/0/0
description USER;
unit 0 {
family ethernet-switching {
interface-mode trunk;
vlan {
members all;
}
}
}
{master:0} [edit]
user@switch1# show interfaces ge-0/0/1
description MGMT;
unit 0 {
family ethernet-switching {
interface-mode trunk;
vlan {
members all;
}
}
}
{master:0} [edit vlans]
user@switch1# show
data1 {
vlan-id 2;
}
data3 {
vlan-id 134;
}
rpsControl {
vlan-id 3960;
}

## Slide 10: Config – Node
user@switch2> show configuration protocols
protection-group {
ethernet-ring cl-ring-01 {
east-interface {
control-channel {
ge-0/0/0;
}
}
west-interface {
control-channel {
ge-0/0/1;
}
}
control-vlan rpsControl;
data-channel {
vlan [2 134];
}
}
}
Switch2
Switch3
Switch1 RPL Owner
Switch4
X
R-APS
R-APS
ge-0/0/1
ge-0/0/0
{master:0} [edit]
user@switch2# show interfaces ge-0/0/0
description USER;
unit 0 {
family ethernet-switching {
interface-mode trunk;
vlan {
members all;
}
}
}
{master:0} [edit]
user@switch2# show interfaces ge-0/0/1
description MGMT;
unit 0 {
family ethernet-switching {
interface-mode trunk;
vlan {
members all;
}
}
}
{master:0} [edit vlans]
user@switch2# show
data1 {
vlan-id 2;
}
data3 {
vlan-id 134;
}
rpsControl {
vlan-id 3960;
}

## Slide 11: Monitoring ERPS
user@switch> show protection-group ethernet-ring interface
Ethernet ring port parameters for protection group cl-ring-01
Interface Forward State RPL End Signal Failure Admin state
ge-0/0/0 discarding yes clear ready
ge-0/0/1 forwarding no clear ready
Switch2
Switch3
Switch1 RPL Owner
Switch4
X
R-APS
R-APS
ge-0/0/1
ge-0/0/0