## Slide 1: JNCIS-ENT
Layer 2 security and loop prevention

## Slide 2: MAC Limiting and Persistent MAC
Layer 2 security
8

## Slide 3: What If?
Multiple man-in-the-middle attacks can be done by poisoning or overloading ethernet-switching tables
  If too many MACs are learned and overflow the table, all inbound frames to an unknown MAC is treated as BUM traffic
  Duplicate MACs can at best be a mistake and at worst be malicious and cause significant network and security troubles regardless
Administrators can limit the number of MACs which can be seen on a port, or statically set ethernet-switching table entries to limit to specific MACs

## Slide 4: MAC Limiting
MAC limiting allows an administrator to specify the number of MAC addresses which may be learned on a given port
  The primary purpose of the functionality is to protect the switch and other network resources from attack
An arbitrary number of MACs may be limited to a port
  It is common for 2 MACs to be allowed per port for environments with VoIP
user@switch1> show configuration switch-options
interface {
ge-0/0/0.0{
interface-mac-limit {
2;
packet-action log;
}
}
}
user@switch1> show configuration vlans default
vlan-id 1;
switch-options {
interface-mac-limit {
2;
}
}

## Slide 5: MAC Limiting Cont.
The administrator can also specify which source MAC addresses will be accepted on each interface
user@switch1> show configuration interfaces
ge-0/0/0 {
unit 960 {
accept-source-mac {
0f:ab:12:0e:95:ab;
}
family ethernet-switching {
interface-mode access;
vlans {
members data;
}
}
}
}

## Slide 6: MAC Move Limiting
Configuring MAC move limiting will allow the switch to take the configured action if a MAC is learned from different ports the number of times configured per second
  This can help protect against MAC spoofing and mitigate the effects of a layer 2 loop
user@switch1> show configuration vlans default
vlan-id 1;
switch-options {
mac-move-limit 2 packet-action shutdown;
}

## Slide 7: Persistent MAC
Also known as ‘sticky MAC’, persistent MAC learning allows for a switch to dynamically learn a set number of MAC addresses on a port and then retain those learned MAC addresses through reboots
  This can limit the amount of administrative overhead involved with configuring accept-source-mac
user@switch1> show configuration switch-options
interface {
ge-0/0/0.0{
persistent-learning;
interface-mac-limit {
2;
packet-action log;
}
}
}