## Slide 1: JNCIS-ENT
Layer 2 switching and VLANs

## Slide 2: Layer 2 Security Lab
Configuration and Monitoring Layer 2 Security Features
11

## Slide 3: Diagram

## Slide 4: Configuring DHCP Security
Review the starting configuration on SW1 and the DHCP Server
On SW1 configure DHCP Security with ge-0/0/1 set as a trusted interface
Commit and-quit configuration mode on SW1
On PC1 obtain an IP address by DHCP
On SW1 review DHCP security binding and statistics
On the DHCP_Server review the DHCP server statistics
Enable DHCP Server on ROGUE_DHCP
On PC1 obtain another IP address by DHCP
On SW1 review DHCP security statistics

## Slide 5: Configuring DAI
On ROGUE_DHCP configure ge-0/0/0.0 with the IP address 10.0.0.101/24 and commit
Ping PC1 from ROGUE_DHCP
On SW1 configure ARP inspection and commit
On ROGUE_DHCP clear the ARP table and attempt to ping PC1 again
On SW1 review the DAI statistics
On PC1 attempts to ping ROGUE_DHCP
On SW1 review the DAI statistics again for changes

## Slide 6: Configuring L2 Firewall
On vPC
Start a continuous ping to DHCP_Server
On vEX
Configure a layer 2 firewall filter to block all traffic sourcing from vPC’s IP address
Apply the layer 2 firewall filter ingress on the LAN VLAN and commit
On vPC
Cancel ping and attempt again to validate effect
On vEX rollback to previous config and attempt to ping again to validate