## Slide 1: JNCIS-ENT
Protocol Independent Routing

## Slide 2: Martian Addresses
Invalid routes
2

## Slide 3: What is a Martian route?
A Martian route is non-routable
  These are reserved address spaces by default. They are ignored by the routing table if any protocol or configuration attempts to insert them.
First mentioned in RFC1208
  Similar to Bogons, although slightly different. Both reference similar IP space and overall bad routing information
IPv4 Default Martian Addresses
0.0.0.0/8 orlonger
127.0.0.0/8 orlonger
192.0.0.0/24 orlonger
240.0.0.0/4 orlonger
IPv6 Default Martian Addresses
Loopback address
Reserved and unassigned from RFC2373
Link-local unicast prefixes

## Slide 4: Configuring Martian Routes
Additional routes may be manually configured. These routes will be ignored in the RIB
lab@SW1# show routing-options
martians {
10.10.10.0/24 orlonger;
10.10.20.0/24 exact;
10.10.30.0/24 through 10.10.33.0/24;
}
lab@SW1# set routing-options martians 10.10.30.0/24 ?
Possible completions:
exact Exactly match the prefix length
longer Mask is greater than the prefix length
orlonger Mask is greater than or equal to the prefix length
prefix-length-range Mask falls between two prefix lengths
through Route falls between two prefixes
upto Mask falls between two prefix lengths

## Slide 5: Monitoring Martian Routes
lab@SW1> show route martians
inet.0:
0.0.0.0/0 exact -- allowed
0.0.0.0/8 orlonger -- disallowed
127.0.0.0/8 orlonger -- disallowed
192.0.0.0/24 orlonger -- disallowed
240.0.0.0/4 orlonger -- disallowed
224.0.0.0/4 exact -- disallowed
224.0.0.0/24 exact -- disallowed
10.10.10.0/24 orlonger -- disallowed
10.10.20.0/24 exact -- disallowed
10.10.30.0/24 through 10.10.33.0/24 -- disallowed