## Slide 1: JNCIS-ENT
Protocol Independent Routing

## Slide 2: Load Balancing
Implementing and monitoring layer 3 load balancing
4

## Slide 3: Equal Cost Multi-pathing
Allows for the equal distribution of traffic over multiple paths with an equal cost to the destination
  Can be configured to load-balance on a per packet or a per flow basis
Junos does not perform load-balancing by default
  One of the available next-hops are selected and used for all traffic to the destination

## Slide 4: Per-Packet vs. Per-Flow
Per-packet distribution alternates equal cost paths in a round-robin fashion, with each packet routed to the next-hop currently selected in the alternation
  Due to differences in latency between the paths, this can result in packets arriving out of order
Per-flow distribution routes all packets associated with a flow through a single next-hop
  All modern Junos platforms perform per-flow, much better for real-time applications like voice and video
Packet 1
Flow 1
Flow 2
Packet 3
Packet 2
Packet 4
Flow 2
Flow 1

## Slide 5: Configuring Load Balancing
lab@SW1# show policy-options
policy-statement load_balance_all {
then {
load-balance per-packet;
}
}
lab@SW1# show policy-options
policy-statement load_balance_some {
from {
route-filter 10.22.33.0/26 orlonger;
}
then {
load-balance per-packet;
}
}
All routes may be considered for load balancing, or only a subsection by route-filter
  Due to differences in latency between the paths, this can result in packets arriving out of order
The per-packet option in the ‘then’ statement does not actually mean it will be load balanced on a per-packet basis.
  Older platforms perform per-packet, however all modern Junos platforms perform per-flow load balancing

## Slide 6: Applying Load Balancing
lab@SW1# show routing-options
forwarding-table {
export load_balance_all;
}
All routes may be considered for load balancing, or only a subsection by route-filter
  Due to differences in latency between the paths, this can result in packets arriving out of order
Applying a load balancing policy will only affect the forwarding table, the routing table remains unaffected
RT
FT
FT
Routing Engine
Packet Forwarding Engine
Export policy

## Slide 7: Monitoring Load Balancing
lab@SW1# run show route forwarding-table
Routing table: default.inet
Internet:
Destination Type RtRef Next hop Type Index NhRef Netif
default perm 0 rjct 36 1
0.0.0.0/32 perm 0 dscd 34 1
10.11.12.0/24 user 0 ulst 262142 2
192.168.2.1 ucst 564 3 ge-0/0/0.0
192.168.2.2 hold 595 3 ge-0/0/0.0
10.22.33.0/26 user 0 rtbl 587 3
10.22.33.1/32 intf 0 10.22.33.1 locl 565 1
10.22.33.2/32 user 0 10.22.33.2 locl 590 3
192.168.2.0/24 intf 0 rslv 557 1 ge-0/0/0.0
192.168.2.0/32 dest 0 192.168.2.0 recv 555 1 ge-0/0/0.0
Notes: Note the 2 next-hops for the destination